## Slide 1: Marine Electronics, Power
Eric Steinberg - Farallon Electronics

## Slide 2: Agenda
Common Problems - usually have common sense solutions
The Power Plan

## Slide 3: Common Problems and Solutions
80% of failures are installation related
  If it were a car, we would call it a lemon
  Keep the water out
Inspect everything
  EVERYTHING
Workmanship
  Dishes in your cupboard (whaaat?)
Keep complexity below your pain threshold
Know your systems, labels and drawings are helpful!

## Slide 4
VHF antenna connector in the bilge area

## Slide 5
Open terminal strip
near the floor

## Slide 6: Common Problems and Solutions
80% of failures are installation related
  If it were a car, we would call it a lemon
  Keep the water out
Inspect everything
  EVERYTHING
Workmanship
  Dishes in your cupboard (whaaat?)
Keep complexity below your pain threshold
Know your systems, labels and drawings are helpful!

## Slide 7: Common Problems and Solutions
80% of failures are installation related
  If it were a car, we would call it a lemon
  Keep the water out
Inspect everything
  EVERYTHING
Workmanship
  Dishes in your cupboard (whaaat?)
Keep complexity below your pain threshold
Know your systems, labels and drawings are helpful!

## Slide 8
Chaos

## Slide 11
Peace and harmony

## Slide 13
Ta Da

## Slide 14: Common Problems and Solutions
80% of failures are installation related
  If it were a car, we would call it a lemon
  Keep the water out
Inspect everything
  EVERYTHING
Workmanship
  Dishes in your cupboard (whaaat?)
Keep complexity below your pain threshold
Know your systems, labels and drawings are helpful!

## Slide 15: Common Problems and Solutions
80% of failures are installation related
  If it were a car, we would call it a lemon
  Keep the water out
Inspect everything
  EVERYTHING
Workmanship
  Dishes in your cupboard (whaaat?)
Keep complexity below your pain threshold
Know your systems, labels and drawings are very helpful!

## Slide 16: Pac Cup Power Plan
Power Plan Template
  www.pacificcup.org >
  RESOURCES >
  Knowledgebase >
  Energy Management
How to find the information you need
  Forget the spec sheets, test it yourself
  Energy monitor with shunt
Appropriate redundancy/contingency/spares
  Wire offcuts, connectors, tape, tools, belts, shear pins
Power production issues , failures

## Slide 17
2012 Sample Energy Budget.xls

## Slide 18: Mas

## Slide 19: Pac Cup Power Plan
Template
  www.pacificcup.org >
  RESOURCES >
  Knowledgebase >
  Energy Management
How to find the information you need
  Forget the spec sheets, test it yourself
  Energy monitor with shunt
Appropriate redundancy/contingency/spares
  Wire offcuts, connectors, tape, tools, belts, shear pins
Power production issues , failures

## Slide 21: Pac Cup Power Plan
Template
  www.pacificcup.org >
  RESOURCES >
  Knowledgebase >
  Energy Management
How to find the information you need
  Forget the spec sheets, test it yourself
Appropriate redundancy/contingency/spares/tools
  Wire offcuts, connectors, NMEA2000, tape, tools, belts, shear pins
  Multimeter, clamp meter
Power production issues , failures

## Slide 22: Pac Cup Power Plan
Template
  www.pacificcup.org >
  RESOURCES >
  Knowledgebase >
  Energy Management
How to find the information you need
  Forget the spec sheets, test it yourself
Appropriate redundancy/contingency/spares
  Wire offcuts, connectors, tape, tools, belts, shear pins
Power production issues, failures

## Slide 23: Testing and Seatrials
Test test test
  Alternator output rating
  Seatrials
  Seat time, email, radios, AIS, computer
Get it done early

## Slide 24: Testing and Seatrials
Test test test
  Alternator output rating
  Seatrials
  Seat time, email, radios, AIS, computer
Get it done early

## Slide 25: Communications
Satellite
  Starlink
    Flat High Performance
  Iridium
    GO! Email / text / phone
    GO Exec Email / text / phone / internet (IP)
    Certus Email / text / phone / internet (IP)
  Inmarsat
SSB and Modem
  Not monitored in 2024, useful for emergency
VHF and AIS
  Not required 24/7, but a good idea
  DSC
  Emergency antenna required
  Coax loss calculator

## Slide 26: Communications
Satellite
  Starlink
    Big
    100w
    Extra parts for DC
    Voice comms
    VOIP/SIP
    Wifi calling

## Slide 27: Communications
Satellite
  Starlink
  Iridium
    GO! Email / text / phone
    GO Exec Email / text / phone / internet (IP)
    Certus Email / text / phone / internet (IP)
  Inmarsat
SSB and Modem
  Not monitored in 2024, useful for emergency
VHF and AIS
  Not required 24/7, but a good idea
  DSC
  Emergency antenna required
  Coax loss calculator

## Slide 28: Communications
Satellite
  Iridium
    GO!
    GO Exec
    Certus

## Slide 29: Communications
Satellite
  Iridium
    GO!
    GO Exec
    Certus 100
use LMR-400 coax

## Slide 30: Communications
Satellite
  Starlink
  Iridium
    GO! Email / text / phone
    GO Exec Email / text / phone / internet (IP)
    Certus Email / text / phone / internet (IP)
  Inmarsat
SSB and Modem
  Not monitored in 2024, useful for emergency
VHF and AIS
  Not required 24/7, but a good idea
  DSC
  Emergency antenna required
  Coax loss calculator

## Slide 31: Communications
Satellite
  Starlink
  Iridium
    GO!
    GO Exec
    Certus
  Inmarsat
SSB and Modem
  Not monitored in 2024, useful for emergency
VHF and AIS
  Not required 24/7, but a good idea
  DSC
  Emergency antenna required
  Coax loss calculator

## Slide 32: Communications
Satellite
  Starlink
  Iridium
    GO!
    GO Exec
    Certus
  Inmarsat
SSB and Modem
  Not monitored in 2024, useful for emergency
VHF and AIS
  Not required 24/7, but a good idea
  DSC
  Emergency antenna required
  Coax loss calculator

## Slide 33: Notes
Lemon Law requires a vehicle manufacturer that is unable to repair a vehicle … after a reasonable number of repair attempts to replace or repurchase the vehicle.

## Slide 34: Thanks!
info@farallon.us